## Slide 1: LayerCode: embeds barcode in 3D printed object (additive manufacturing)
Columbia University, Adobe
Henrique Teles Maia, Dingzeyu Li, Yuan Yang, Changxi Zheng

## Slide 2: Discussion with Dr.Zhu
Vuforia跟踪条形码
LayerCode两极（如果用于跟踪是否失效
鲁棒
识别+跟踪+解码 一体化

## Slide 3: 可以做的改进(from sec6. evaluation)
研究鲁棒性：研究编解码方法和识别方法对于遮挡、同色背景的抵抗力（文中研究的基本都是没有遮挡、前背景大对比度）
MOSSE追踪,CNN目标识别（目标有特征，识别目标后画出OBB能避免背景干扰）
研究速度：优化graph-based approach来降低解码时间/解码时间上界 -> feasible on mobile devices
研究信息容量：ternary or quaternary（三元/四元）打印可以提高信息容量
姿态估计

## Slide 4: sec1. introduction
Encoding algorithm
Decoding algorithm (from single photo)
Test with large dataset of virtual rendering (4000+ shapes from Thingi10k dataset 2016, 99% successfully encode & decode)
Embedding optical tags: on, beneath, inside the surf (ref)
Challenges:
robust encoding & decoding:
standard barcode-maps every bit to a bar thickness
we-encode bits based on local change of layer thickness (invariant under diff. orientation)
image-paths along for decoding
2. need to introduce 2 distinguishable layer types:
2 material printer OR diff deposition height OR mix NIR dye

## Slide 5: sec1. introduction
Attributes:
* conventional cam (NIR with filter and light source when detecting)
* redundancy: readable from multiple cam view and even broken
* depth info for free: parallel light pattern -> use structured light tech in CV
how???
Output of encoding algorithm: a series of slices along the printing direction to specify the thickness of each coding layer
Cannot transfer flat barcode’s pattern directly: because of spatially variant
solution: use thickness ratio of 2 consecutive
layers in a local region (because they share
the approx. same surface tangent plane)

## Slide 6: sec3. encoding
Coding scheme details: bn -> an
an: thickness
bn: bit
an+1 : an = 1 if bn+1 = 0
an+1 : an = 1/M or M if bn+1 = 1 the proposed pipeline used M = 2
inverse map for decoding:

## Slide 7: sec3. encoding
Coding scheme details: bn -> an
start of bit string: a layer with an = Nh (the proposed pipeline used M = 4), followed by 2 layer with thickness = h (bit 0 as the head of the bit string)
end of bit string: a single layer appended to form bit 1 as the rear of the bit string, with the last layer is again an = Nh after the appended layer
the bit string always starts with 0 and ends with 1: direction or the barcode can be tell

## Slide 8
sec3. encoding
Error correction: is able to carry any error-correction code as long as enough bit string length (no correction code in experiment to test pure performance)

## Slide 9: Decoding pipeline
Preprocessing: distinguish ‘white bar’ & ‘black bar’
Graph construction
Graph traversal

## Slide 10: sec4. decoding
Image preprocessing: see algorithm 1 & appendix A
1. 2-color printer:
1) intensity thresholding: remaining pixels are either on black or white layer color thresholding???
2) 2-way clustering through GMM in a sliding window: each window produces the label of its central pixel, repeat 3 time with diff. size how???
3) pixel-wise majority vote of labels how???
helpful to convert to LAB/HSV, focus on AB channel when clustering

## Slide 11: sec4. decoding
Image preprocessing: see algorithm 1 & appendix A
2. varying layer height objects:
1) remove the background (color thresholding???) -> greyscale
2) morphological operation:
bottom and top hat filtering -> increase contrast how???
bilateral filter (ref) -> blur black & white layer regions without blurring boundary
GMM-based clustering -> binarize the image how???

## Slide 12: sec4. decoding
4.1 graph construction
Flood fill process -> all pixels are either labelled black or white -> formed black regions & white regions -> each regions is a node, 2 nodes are connected if their regions are adjacent
Edge e (connects node A & B)
vector v of e: denotes general direction to move A -> B
* identify boundary pixels in region A: pixels within \delta pixels away from another region (in paper \delta = 3) how???
* estimate boundary normal direction (quickest direction to get into another region from current boundary pixel (深度优先搜索???)
* v is the avg normal direction over all boundary pixels between A & B

## Slide 13: sec4. decoding
4.1 graph construction
Edge e (connects node A & B)
label r of e:
* thickness estimation: for each boundary pixel p between A & B, find a shortest image plane vector dm between p and another region (not A or B but C) (深度优先搜索???), project dm onto np to estimate thickness of a layer -> now hA(p) & hB(p) are known
* get bn: use 0.5logM as a threshold

## Slide 14: sec4. decoding
4.1 graph construction
Edge e (connects node A & B)
feature label r: indicates the bit of the edge (edge = 1 bit)
unknown M? -> regard x = |loghA - loghB| as a random variable, the distribution of x must be a 2-peak GMM!!! Center 1 at 0, center 2 at logM -> use maximum likelihood estimation to estimate logM (p(logM) in GMM must have highest pdf except for p(0)) h? not imprt., can be set as prior OR encode it in the object
Identify starting & ending nodes: outliers in GMM!!! Use a set S to contain
4.2 decoding through graph traversal
DFS: repeatedly DFS start from a node
in set S. use edge vector to make sure
direction consistency (otherwise: loop)

## Slide 15: sec4. decoding
4.2 decoding through graph traversal
traversal stops: another node in S is reached OR DFS runs out of unvisited(fatal error, because the bit string should always end with bit 0)
4.3 early termination
Terminate the graph traversal if we have surveyed a sufficient number of paths: terminate decoding once num_path ≥ K (num_path is counted in DFS)
Terminate if: Current individual
decoded bits (not string) have
80% in common

## Slide 16: sec4. decoding
4.4 depth recovery
Calibrate the cam in advance: get intrinsic param K
Fix cam: get extrinsic param R, t
4.4 & Appendix B: didn’t understand

## Slide 17: sec5. fabrication
5.1 2-color fabrication (for multi-material 3D printers)
Produce LayerCode without any modification to software/hardware
5.2 variable layer heights
Black layers: h0 for each layer?
white layers: h1 for each layer?
specular high light
green region: spare & granular(颗粒状的
red region: dense & uniform
difference of highlight distribution
-> allows decoding to discern(分辨
2 types of layers in preprocessing

## Slide 18: sec5. fabrication
5.2 variable layer heights
Interweave G-code for h0 and h1 at specific location, to construct alternating printing heights (the paper used h1 as integer multiple of h0, to ensure seamless switches across layer heights)
5.4 discussion on implementation & application
40 min to several hours
2-color & variable layer height: time cost comparable to that w/o LayerCode

## Slide 19: sec6. evaluation
6.1 database construction
4835 Shape meshes from Thingi10k dataset
(ref)
Embed a LayerCode indicating model’s ID
Printing direction: longest dimension
Baseline layer thickness h: set to repeat the tag
3 times
Use Mitsuba(ref) to render the encoded output
Test influence of viewpoint: sample 30
viewpoints

## Slide 20: sec6. evaluation
6.2 result statistics
Camera angle dependency

## Slide 21: sec6. evaluation
6.2 result statistics
Decoding time: seconds-5 min, complexity is derived from graph approach
-graph building operations (image processing, neighbor region dis, masking)
-image resolution
-shapes, holes, occlusions -> number of nodes -> decoding time
-partly because Matlab
-partly because wish to explore sufficient paths for robust decoding
Lower bound of h
Complex shapes: 4791 successful shapes
, 44 failure cases
Stress test
Failure cases

## Slide 22: secX. 代码分析
https://github.com/henriquetmaia/layercode
\layercode\matlab\code

## Slide 23
Robust edge based 3D object tracking with direction-based pose validation
Shandong Univerisity
Bin Wang, Fan Zhong, Xueying Qin

## Slide 24: sec1. introduction

## Slide 25: Monocular Model-Based 3D Tracking of Rigid Objects
Computer Vision Lab, EPFL
Vincent Lepetit, Pascal Fua

## Slide 26: ch2. mathematical tool
2.1 camera representation
Perspective projection model
3D point M = [X,Y,Z]T
2D point m = [u,v]T (correspond to M)
m & M are related by:
here, m_ = [u,v,1] M_ = [X,Y,Z]T
(homogenous coordinates)
projection matrix P: 3x4
cam calibration matrix K: 3x3, depends on internal param of the cam
external param matrix [R|t]: 3x4, rotation matrix R
translation t

## Slide 27: ch2. mathematical tool
2.1 camera representation
Cam calibration matrix
au, av: scale factor in u, v direction
proportional to focal length f
ku & kv: number of pixels per unit dis in u, v direction
principle point c = [u0,v0]T:
skew s: non-zero only if u and v are not perpendicular
* c at centre of img (approximation)
* au = av if pixels are square
calibrated: if internal param K is known

## Slide 28: ch2. mathematical tool
2.1 camera representation
External param matrix (cam pose)
Mw: in world coordinate
Mc = RMw+t: in cam coordinate
for cam centre c: Mc = 0, 0 = RC+t,

## Slide 30
补锅：
PnP
RANSAC

## Slide 31
PVNet, RGB
CVPR2019
Model Based Training, Detection, Pose Estimation
RGBD ACCV2012
Monocular-based 3D Tracking
EPFL
Traditional method
Traditional method
Render for CNN
ICCV2017
Recent CNN based method

## Slide 32
PVNet, RGB
CVPR2019
Model Based Training, Detection, Pose Estimation
RGBD ACCV2012
Traditional method
traditional CV pipelines
Trimmed ICP
BMVC2002
Model alignment
Original ICP
PAMI1992
Calculation of optimal motion
RGB based
FCNN: vector prediction & semantic segmentation
在物体semantic上随机N次，每次2个vector求交得到key point candidate h，
Semantic上所有点根据w公式对h投票（RANSAC，得到等势线
FPS算法pick K points out of N，约束：points on surface
K key points + EPnP：初始化6DOF pose estimation
Levenberg Marquardt + Mahalanobis distance迭代求pose
RGBD based
Based on 3D CAD models
Origin of LINEMOD dataset
Color gradient + surface normal
基于template detection的pose estimation
使用Trimmed ICP匹配P点云和M点云
Model based & model alignment methods
Monocular-based 3D Tracking of Rigid Objects
EPFL
LINEMOD dataset
photogrammetry
RANSAC original
Graphics & Image Processing1981
Robust estimation RANSAC

## Slide 33
2D-3D correspondence & direct pose estimation
Hierarchical Fiducial Marker
Robotics2018
聚焦于hierarchical fiducial marker dictionary
提到了许多古老的基于fiducial marker的AR系统：ARTag，ARToolKit
无遮挡fiducial marker detection & pose estimation pipeline(来自ref)
3D pose estimation for marker for UAVs control
ICRA2010
Homography based pose estiamtion
RANSAC original
Graphics & Image Processing1981
Robust estimation RANSAC
Homography pose estimation base on RANSAC & projection model

## Slide 34
Deep ChArUco: Dark ChArUco Marker Pose Estimation
CVPR2019
DNN for fiducial marker detection
Used PnP(ref20)
2D-3D correspondence & direct pose estimation

## Slide 35
ARToolKitPlus
CV Winter Workshop2007
Robust Planar Pose Tracking (RPP)
PAMI2005
Automatic Thresholding
Fiducial marker Detection pipeline
Pose estimation
2D-3D correspondence & direct pose estimation

## Slide 36
Monocular-based 3D Tracking of Rigid Objects
EPFL
mathematical tool
perspective projection model & camera parameters
camera pose parameters: Euler Angle & Quaternion & Exponential Map
estimating external parameter [R,t]: DLT & PnP & estimation from 3D plane
& nonlinear projection error
Least Square & Newton-based minimization algorithm
robust estimation: M-estimator & RANSAC
Bayesian Tracking: Kalman Filtering & Particle Filtering

## Slide 38
Key point
PnP类工具箱
RANSAC类工具
3D model
2D image
MOSSE跟踪